## Slide 1: Enhancing Seismic Safety in Munich's Geothermal Energy Sector: Data-driven Model Updating for Building Vibrations under Induced Seismicity
M.Sc. Wei-Teng, Kao
Technical University of Munich
TUM School of Engineering and Design
Chair of Structural Mechanics
Munich, 23.09.2024

## Slide 2: Proposed framework of the MDSI project
Current focusing part

## Slide 3: System identification during operation
Two different system identification methods are used, which are SSI-COV and Single Sensor Identification (SSI).
Practically, SSI-COV could provide us with more accurate results than the SSI method. However, SSI-COV requires multiple channel measurements.
SSI might be too sensitive since it is based on frequency domain decomposition (FDD), which ideally used for multiple-output problem
In our case, we have only one sensor( geophone) on each floor, which is practically not enough for operational modal analysis (OMA)
SSI-COV method is quite sensitive to parameters, different setups of parameters might lead to different results

## Slide 4: System identification using SSI from 75 events
* System identification using SSI methods. Two modes are collected for each event, where only the events that both sensors in 1OG and 2OG are activated simultaneously will be counted, the number of events is N = 75.
Detected dominated frequency against damping ratio, 1OG
Detected dominated frequency against damping ratio, 2OG

## Slide 5: System identification using SSI-COV from 75 events
* System identification using SSI-COV methods. A number of modes are automatically detected for each event, where only the events that both sensors in 1OG and 2OG are activated simultaneously will be counted; the number of events is N = 75.
Detected system in x dir.
Detected system in y dir.
Detected system in z dir.

## Slide 6: System identification by hammer testing
Hammer testing belongs to the Experimental Modal Analysis (EMA) method, which could provide us with more accurate results than OMA.
In our experiment, four accelerometers are installed at each floor slab and three on the wall; I only focus on the accelerometers installed at each floor slab, which total 8 accelerometers.
The signal received from the sensor on the wall is relatively small compared to the signal received from the sensor on the slab. Therefore, I ignored them in my analysis.
The Location of measurement and excitation will be reported in the next slide.
Since the simulation will return the displacement signal, I transfer the experiment data from acceleration to displacement.

## Slide 7: Hammer testing: excitation points
Coordinates of Excitation points:
Position 1 (ID: EX22) : [9.30, 5.90, Z]
Position 2 (ID: EX221) : [12.77, 2.748, Z]
Position 3 (ID: EX220) : [7.19 , 8.14, Z]
More than three tests are applied on each excitation point.
The Z in coordinates indicates the height of the second floor, which is one of the parameters that will be updated.
X
Y

## Slide 8: Hammer testing: measurement points
X
Y
X
Y
10
11
12
9
3
13
14
15
Uniaxial
Triaxial
Geophone

## Slide 9: System identification by hammer testing, location 1 (ID: EX22)
*The ID in the label indicates the ID of the channel. On the first floor, the channels are 9,10,11,12, and on the second floor, it is 3,13,14,15
* Here, only plot the imaginary part of the FRF since the imaginary part can be used to detect the mode shape

## Slide 10: System identification by hammer testing, location 2 (ID: EX221)
*The ID in the label indicates the ID of the channel. On the first floor, the channels are 9,10,11,12, and on the second floor, it is 3,13,14,15
* Here, only plot the imaginary part of the FRF since the imaginary part can be used to detect the mode shape

## Slide 11: System identification by hammer testing, location 3 (ID: EX220)
*The ID in the label indicates the ID of the channel. On the first floor, the channels are 9,10,11,12, and on the second floor, it is 3,13,14,15
* Here, only plot the imaginary part of the FRF since the imaginary part can be used to detect the mode shape

## Slide 12: ANSYS model in python
Building parameter, N = 26
SSI parameter, N = 3

## Slide 13: Harmonic analysis
For each parameter setups from DOE, three harmonic analysis are performed based on three different excitation points.
To mimic the hammer testing, the unit force load on z direction will be inputted.
The frequency response functions (FRFs) extracted from 8 measurement points will be compared with FRFs from hammer test for FEM update.
Using the Mode superposition (MSUP) method to accelerate the simulation. Compared to FULL method, it can approximately accelerate the simulation by 2X.
Two different cases are tested, one with Soil structure interaction, another one without.
mapdl.f(excitation_node,"FX",0)
mapdl.f(excitation_node,"FY",0)
mapdl.f(excitation_node,"FZ",1)

## Slide 14: FRFs from initial guess parameter sets, x=np.zeros(19,1)

## Slide 15: DOE and the range of parameter varying.
Using LHS for sampling
Assuming that there are 19 parameters need to be updated and the Poisson's ratios are fixed
Size of DOE, N = 1000
Assume the Vary_ratio = 0.5
X_transformed follows uniform distribution and in the range of [-1,1]

## Slide 16: FEM update proposal

## Slide 17: Selecting qualified datasets from further training and testing.
Only focus on the top two dominated frequencies, which are approximately 12 Hz and 18.5 Hz, according to FRFs from the hammer test.
According to the imaginary part of the FRFs, we can observe that mode shapes at 12 Hz are all in the same direction for both floors; However, the mode shape at 18 Hz shows the opposite for each floor; this will be a crucial indicator for detecting the correct mode shape from the simulation.
Using MAC to check the similarity of mode shape from testing and simulation.
For each simulation, If the MAC of each dominated frequency is less than 0.4, then it will be ignored. This is because some combination of the parameter sets might lead to peak overlapping, which will decrease the quality of collected training data.

## Slide 18: Surrogate model accuracy for each dominated frequency

## Slide 19: Forming the objective function:
Using LHS for sampling the population of GA.
Used GA as a “Warm start”; the top 10 candidates are extracted, followed by fine-tuning using the L-BFGS-B algorithm.
After fine-tuning, the top 10 candidates might converge to some specific region. We delete the repeated datasets and perform simulations based on the remaining datasets.
Compare the FRFs from simulation with experimental FRFs directly, and return the one with less error. The error is computed as error = (H_simu(f) – H_exp(f))^2.

## Slide 20: GA + L-BFGS-B return parameter sets
X best = [0.89822568 0.58375721 0.56752307 0.28733618 0.59190536 0.88966501 0.35375698 0.20869523 0.23823104 0.06890725 0.86540033 0.72964186 0.89093788 0.60733761 0.50450945 0.81033345 0.83931667 0.66696147 0.62083669]

## Slide 21: After FEMU

## Slide 22: Current issues
Focus only on the first and second-dominated frequencies.
  -> The scaling between FRFs from simulation and hammer testing can not be considered.
  ->If there is any other peak appears, its effect will not be considered.
This method cannot find the global minimum; the result will converge but will be different all the time if the random seed is not fixed. However, it should report a potential range of each parameter.

## Slide 23: Sensitivity based FEMU:
Not working, due to an underdetermined system
[1]: Improved finite element model updating of a fullscale steel bridge using sensitivity analysis
[2]: The sensitivity method in finite element model updating: A tutorial